An Attempt to Reproduce the Old Energy Spectrum
Collimator in cruddy location: line of sight from beam window
6 cm x 6 cm beam veto
5 cm x 5 cm target

---
What are we trying to reproduce?

---
Our graphs....

---
Particle Composition

---
Particle Composition
E800ns>250 keV
	Muons	Protons	Electrons	Photons	Deuterons	Tritons	Alphas	Other
PP/BV	0.0%	26.1%	42.3%	0.0%	1.4%	0.1%	6.4%	23.8%
NoSi	0.0%	20.8%	72.9%	0.0%	1.3%	0.2%	3.9%	0.9%
MuStp	0.0%	30.3%	61.7%	0.0%	1.5%	0.2%	5.3%	1.0%
E800ns>2 MeV
	Muons	Protons	Electrons	Photons	Deuterons	Tritons	Alphas	Other
PP/BV	0.0%	49.9%	20.9%	0.0%	3.1%	0.2%	20.5%	5.4%
NoSi	0.0%	63.3%	17.8%	0.0%	4.3%	0.6%	13.0%	1.0%
MuStp	0.0%	67.8%	13.5%	0.0%	3.7%	0.7%	13.2%	1.0%

---
Rates
No cuts in these rates plots other than time

---
Possible Current Setup
10 cm veto
10 cm target
More shielding upstream
Lead lining downstream (180 degree coverage plus half the roof)
First we'll look at a chamber without the lining

---
Spectrum

---
Particle Composition

---
Particle Composition
E800ns>250 keV
	Muons	Protons	Electrons	Photons	Deuterons	Tritons	Alphas	Other
PP/BV	0.0%	18.8%	73.7%	0.0%	1.9%	0.2%	4.4%	1.0%
NoSi	0.0%	18.8%	73.8%	0.0%	0.2%	1.9%	4.4%	0.9%
MuStp	0.0%	23.0%	68.6%	0.0%	2.3%	0.2%	5.3%	0.5%
E800ns>2 MeV
	Muons	Protons	Electrons	Photons	Deuterons	Tritons	Alphas	Other
PP/BV	0.0%	45.9%	36.1%	0.0%	5.7%	0.5%	11.6%	0.2%
NoSi	0.0%	45.9%	36.2%	0.0%	0.5%	5.7%	11.6%	0.2%
MuStp	0.0%	58.3%	19.0%	0.0%	7.2%	0.6%	14.7%	0.1%

---
Rates (again, without the lining)

---
Rates (with lining)

---
Rates (90 Degree setup)

---
Conclusions thus far
- Further shielding upstream a necessity, though this is not news to anyone
- Lead lining downstream may not be necessary even with thin target
- 90 degree setup seems a bit better for the proton rates, still have to check particle spectrum